WST-212 – Wireless Door/Window Sensor with Bypass

Specifications:

Transmit Frequency:   345.000 MHz

Frequency Tolerance: 	+/- 15kHz

Bandwidth:  24kHz

Protocol: Honeywell 5800 series (non-encrypted)

Supervisory Interval: 64 min

Battery Type: 1 x CR2032

Battery life: 5 years typical

Operating temp: 32°-120°F (0°-49°C)

Operating humidity: 5-95% RH non condensing

Weight: 1.0 oz

Dimensions: 2.25 x 1 x 0.25 inches

Color: White and brown cases

Bypass button: Default off (includes non-bypass covers)

Magnet Dimensions: 1.37 x 0.5 x .25 in

Magnet Type: N48 rare earth

Magnet Gap: 5/8th in maximum

Mounting options: 3M VHB double sided tape

Approvals: FCC /IC, ETL

Carton quantity: 60

Master shipping quantity: 240

Universal Electronics’ Ecolink branded Wireless Door & Window Sensor eclipses all others with its thoughtful design specifically for the dealers business. The sensor provides optimal RF range, and fast, reliable detection, alerting 345Mhz and 433Mhz compatible security control panels. Unlike other solutions, this sensor’s low profile design makes it the thinnest sensor on the market, and provides installers brown/white color options in each box to easily blend into the decor of any home. Unmatched inventory cost savings. Includes a 5 year battery life, 2 year warranty and the best price, directly from Ecolink.