WST-702 – Wireless Pet Immune Motion Detector

Specifications:

Transmit Frequency:   345.000 MHz

Frequency Tolerance: 	+/- 15kHz

Bandwidth:  24kHz

Protocol: Honeywell 5800 series (non-encrypted)

Supervisory Interval: 64 min

Coverage: 40 ft x 40 ft

Pet Immunity: 50 lbs

White Light Immunity: 2000 Lux (EN50131-2-4)

Battery Type: 1 x CR123A

Battery life: 5 years typical

Operating temp: 32°-120°F (0°-49°C)

Operating humidity: 5-95% RH non condensing

Weight: 4 oz

Dimensions: 3.62 x 2.62 x 1.5 inches

Color: White

Mounting options:  Screws

Approvals: FCC /IC,

Carton quantity: 10

Master shipping quantity: 60

Coverage Patterns